| 中文產品名稱及別名： | LED鋁燈條 (便利貼燈條) |
| --- | --- |
| 英文產品名稱及別名： | LED Aluminum Light-bar |
| 產品型號： | ID-LB06-DC12/24 |
| 中文產品說明： | vitaLED的LED燈管具有高流明輸出,簡單而精緻的設計適用於辦公室、會議室和住宅照明,我們可提供 一般消費者簡易安裝型(變壓器內置)和商業專用安裝型(變壓器外置)燈管。 無紫外線及紅外線 鋁殼散熱佳, 壽命超過三萬小時,省電50% 兩端附工母DC接頭, 可串接使用 背面附強力磁鐵, 可吸附於各式鐵架、車輛、工作桌、鐵櫃 技術規格: 尺寸 576 x 24 x 11.3mm (1ft’/ 3ft’可訂製) 光輸出標準值 (流明) 850lm / 800lm 色溫CCT (K) 6000 / 3000 / Others 演色性(CRI) 75 耗電及功率因數 10W 發光角度 及 光罩類型 140 度 LED類型及使用顆數 表面黏著型3020/3528 , 120燈 |
| 英文產品說明： | vitaLED’s LED lightbar features high lumen output. The simple and exquisite design is suitable for office, conference room and residential lighting. We offer DC12v and DC24V models for both consumer use and commercial installation. 1. Bulid-in ultra-brightness LED, without UV and IR 2. Aluminum housing, excellent heat dissipation, life Span > 30,000hrs., power saving > 50% 3. Build-in DC connectors at 2 side, easy to connect 4. With powerful magnets in aluminum case, easy to install on shelf, vehicles, working table and desk, iron cabinet, any iron surface . 5. RoHS compliant and CE/FCC safety approval 6. Technical Specification: Size 576 x 24 x 11.3mm (1ft’ / 3ft’ available) Typical Output (lm ) 850lm / 800lm CCT (K) 6000 / 3000 / Others CRI 75 Power (W) & Power Factor 10W View Angle & Lens Type 140 。 LED Type and Q’ty SMD 3020/3528 x 120pcs |