| 中文產品名稱及別名： | 車用迷你警示燈 |
| --- | --- |
| 英文產品名稱及別名： | LED mini-Warning Light for Vehicle |
| 產品型號： | WL-Mini6(9)-W/R/G/B/A |
| 中文產品說明： | 產品特點 標準型6 LED, 內建Rebel LED,可選白/紅/藍/綠/黃光 採用抗UV燈罩, 預留9呎電線 30種閃爍模式, 若安裝雙燈¸可同步閃爍, 有記憶功能 DC10-30V適合各種車輛使用 1英吋崁入孔適用, 採鋁底板可加強散熱 IP68防水處理 產品規格 輸入電壓: DC10-30V 輸入電流: 2.3安培 耗電: 18W(6燈) / 27W(9燈) |
| 英文產品說明： | 1. Design Feather (a) 2 Modules Available , 6 LEDs Standard (9 LEDs for next Generation) Rebel LEDs: White / Red / Blue / Green /Amber (b) UV Stabilized Polycarbonate Lens and 9ft Cable (c) 30 Flashing Patterns, multiple Heads can be synchronized (d) Universal Fit for all Vehicles (e) Mounts in a 1" Hole (the same size as a strobe tube) with Aluminum Base and Advanced thermal Heat Management System (f) Self-contained and Sealed Control Module - No Needs for a Separate Flasher Module (j) Easy Installation: Two Screws Hold the Lamp Securely in Place (k) IP68 Waterproof Certified 2. Specifications: (a) Input Voltage 10 to 30 Volts DC (b) Input Current 2.3 Amps Peak (c) Output Power 18Watt (27W for 9 LEDs Module) |