| 中文產品名稱及別名： | LED植物栽培燈管(T8) |
| --- | --- |
| 英文產品名稱及別名： | LED Agriculture Grow Light Tube (T8) |
| 產品型號： | Size 2ft’(580mm) 2ft’(598mm) 4ft’ (1198mm) P/N GL-TB06-ACuni GL-TB06-ACuni GL-TB-12-ACuni a |
| 中文產品說明： | 1. 專業省電型LED植物燈管(G13腳座), 2. 內建變壓器, 適用於傳統T8螢光燈管燈具 3. LED波長:紅光660奈米 / 藍光455奈米 / 綠光530奈米 4. LED配比(R:G:B) = (a) 6:0:3 / (b) 8:0:1 / (c) 6:2:1 / (d) 其他 5. 標準尺寸: 2呎(595/580mm) / 2呎(603/598mm) / 4呎(1212/1198m), Ø31.6mm 6. 輸入電壓: AC100- 240V (全電壓) 7. 光罩類型: 140度, (a) V溝型, (b) 全透明型 8. 預估壽命: 30,000小時 9. 工作環境: -30~50度C 10.適合場所: 一般家庭, 花店冰櫃, 水草藻類養殖, 植物工廠, 溫室立體層架, 其他 |
| 英文產品說明： | Professional LED Agriculture Grow Tube (G13 Socket) Built-in transformer, fit to traditional fluorescent T8 lampholder LED Wavelength: Red,660nm / Blue,450nm / Green,530nm R.G.B. Ratio: (a) 6:0:3 / (b) 8:0:1 / (c) 6:2:1 (d) Others Standard Size: 2ft’(595/580mm) / 2ft’(603/598mm) / 4ft’(1212/1198m), Ø31.6mm Input Voltage: AC100-240V (universal) Cover Lens : 140。, (a) V-cut type, (b) Clear type Life Span: 30,000 hours Work Environment: -30~50。C Application: General Household, Florist Freezer, Aquatic & Algae Farming, Plant Factory, Three-dimensional (3D) shelf of greenhouse, Other Bio-lighting |