| 中文產品名稱及別名： | LED植物栽培燈管(可串接型) |
| --- | --- |
| 英文產品名稱及別名： | LED Agriculture Grow Light Tube (Connectable) |
| 產品型號： | Size 2ft’(600mm) 4ft’ (1200mm) P/N GL-TB06-DC24(DC12) GL-TB-12-DC24(DC12) a |
| 中文產品說明： | 1.專業省電型LED植物燈管(可串接式) 2.照射角度可調設計,底座附強力磁鐵,易安裝 3.LED波長:紅光660奈米 / 藍光455奈米 / 綠光530奈米 4.LED配比(R:G:B) = (a) 6:0:3 / (b) 8:0:1 / (c) 6:2:1 / (d)其他 5.標準尺寸: 2呎(600mm) / 4呎(1200mm), Ø36mm 6.輸入電壓: DC 24V 或 DC12V 7.光罩類型: 140度, (a) V溝型, (b) 全透明型 8.預估壽命: 30,000小時 9.工作環境: -30~50度C 10.適合場所: 一般家庭, 花店冰櫃, 水草藻類養殖, 植物工廠, 溫室立體層架, 其他 |
| 英文產品說明： | Professional LED Agriculture Grow Tube (Connectable) Rotatable hinge with powerful magnets, easy to installation and adjust projecting direction. LED Wavelength: Red,660nm / Blue,450nm / Green,530nm R.G.B. Ratio: (a) 6:0:3 / (b) 8:0:1 / (c) 6:2:1 (d) Others Standard Size: 2 ft’ (600mm) / 4 ft’ (1200mm), Ø36mm Input Voltage: DC24V or DC12V Cover Lens: 140。, (a) V-cut type, (b) Clear type Life Span: 30,000 hours Work Environment: -30~50。C Application: General Household, Florist Freezer, Aquatic Algae Farming, Plant Factory, Three-dimensional (3D) shelf of greenhouse, Other Bio-lighting |