| 中文產品名稱及別名： | LED水族燈管(T8)(低電壓) |
| --- | --- |
| 英文產品名稱及別名： | LED Aquarium Light Tube (T8)(Low Voltage) |
| 產品型號： | Size 1 ft’(330mm) 2ft’(580mm) 3ft’(895mm) 4ft’ (1198mm) P/N AQ-TB-03-DC12(24) AQ-TB06-DC12(24) AQ-TB09-DC12(24) AQ-TB-12-DC12(24) A |
| 中文產品說明： | 1. LED水族燈管(T8), 變壓器外置型 2. 限用DC12或24V LED專用燈具 3. LED規格: 紅光630奈米 / 藍光455奈米 / 綠光530奈米 / 白光7000K 4. LED比例: 全紅光, 全藍光, 全白光, 三波長 5. 標準尺寸: 1呎(330mm) / 2呎(580mm) / 3呎(895mm) / 4呎(1198m), Ø31.6mm 6. 輸入電壓: 直流12或24V 7. 光罩類型: 140度, (a) V溝型, (b) 全透明型 8. 預估壽命: 30,000小時 9. 工作環境: -30~50度C 10.適合場所: 淡水魚缸, 海水魚缸, 水草缸, 軟體缸, 爬蟲與兩棲類照明, 生物照明 |
| 英文產品說明： | LED Aquarium Light Tube, isolated power supply Fits to 12V or 24V aqua-light system LED Wavelength: Red,630nm / Blue,450nm / Green,530nm / White, 7000K R.G.B. Ratio: Full Red / Full Blue / Full White / RGB-mix Standard Size: 1ft’(330mm) / 2ft’(580mm) / 3ft’(895mm) / 4ft’(1198m), Ø31.6mm Input Voltage: DC12V or 24V Cover Lens: 140。, (a) V-cut type, (b) Clear type Life Span: 30,000 hours Work Environment: -30~50。C Application: Tropical fish & aquatic tank, Marine fish & coral tank, Reptile & amphibians lighting, Bio-lighting |